## Slide 1: Modeling flow and transport in nanofluidic devices
Brian Storey (Olin College)
Collaborators:
Jess Sustarich (Graduate student, UCSB)
Sumita Pennathur (UCSB)

## Slide 2: First…. the 30,000 foot view

## Slide 3: Microfluidics – Lab on a chip ca. 1990
Microfluidics deals with the behavior, precise control and manipulation of fluids that are geometrically constrained to a small, typically sub-millimeter, scale. (Wikipedia)
Stephen Quake, Stanford
Thorsen et al, Science, 2002
Micronit

## Slide 4
Dolomite
Dolomite
Prakash & Gershenfeld, Science, 2007
Seth Fraden, Brandeis
Agresti et al, PNAS 2010

## Slide 5
Nagrath et al, Nature 2007
Circulating tumor cells, MGH
H1N1 Detection, Klapperich BU
Neutrophil Genomics, MGH
Kotz et al, Nature Med. 2010
CD4 cell count, Daktari Diagnostics

## Slide 6: “Hype cycle”
Gartner Inc.
Microfluidics?
Nanofluidics?

## Slide 7: Nanofluidics
Nanofluidics is the study of the behavior, manipulation, and control of fluids that are confined to structures of nanometer (typically 1-100 nm) characteristic dimensions. Fluids confined in these structures exhibit physical behaviors not observed in larger structures, such as those of micrometer dimensions and above, because the characteristic physical scaling lengths of the fluid, (e.g. Debye length, hydrodynamic radius) very closely coincide with the dimensions of the nanostructure itself. (Wikipedia)

## Slide 8: Nanofluidics is interesting because…
Faster, cheaper, better– analogy to microelectronics.
“the study of nanofluidics may ultimately become more a branch of surface science than an extension of microfluidics.” George Whitesides

## Slide 9: Some background. Flow in a channel.

## Slide 10: Pressure driven flow is difficult at the nanoscale
High pressure
Low pressure
Pressure driven flow of a Newtonian fluid between parallel plates has a parabolic velocity profile. The fluid velocity is zero at the walls and is maximum along the centerline.
H
About 100 atmospheres of pressure needed
to drive reasonable flow in typical channels

## Slide 11: The electric double layer
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
+
counter-ions
co-ions
-
-
-
-
-
-
-
Glass + water
Glass
Salt water
Debye length is the scale where concentrations of positive and negative ions are equal.

## Slide 12: Electroosmosis (200th anniversary)
Electric field
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
+
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
+
+
+
-
-
+
+
-
-
+
+
-
-
-
-
-
-
-

## Slide 13: Double layers are typically small ~10 nm Velocity profile in a 10 micron channel
Helmholtz-Smolochowski

## Slide 14: Electroosmosis-experiments
Pressure-driven
Electrokinetic
Molho and Santiago, 2002

## Slide 15: The specific problem – Detection.

## Slide 16: FASS in microchannels
Low cond. fluid
High cond. fluid
High cond. fluid
V
+
Chien & Burgi, A. Chem 1992
σ=10
σ=10
σ=1
E=1
E=10
E Electric field
σ Electrical conductivity

## Slide 17: FASS in microchannels
-
-
-
-
-
-
-
-
-
Low cond. fluid
High cond. fluid
High cond. fluid
Sample ion
V
+
Chien & Burgi, A. Chem 1992
-
σ=10
σ=10
σ=1
E=1
n=1
E=10
E Electric field
σ Electrical conductivity
n Sample concentration

## Slide 18: FASS in microchannels
V
+
Chien & Burgi, A. Chem 1992
-
-
-
-
-
-
-
-
-
Low cond. fluid
High cond. fluid
High cond. fluid
Sample ion
-
E=1
n=1
n=10
σ=10
σ=10
σ=1
E=10
E Electric field
σ Electrical conductivity
n Sample concentration

## Slide 19: FASS in microchannels
-
-
-
-
-
-
-
-
-
Low cond. fluid
High cond. fluid
High cond. fluid
Sample ion
V
+
Chien & Burgi, A. Chem 1992
-
Maximum enhancement in sample concentration is equal to conductivity ratio
E=10
E=1
n=10
σ=10
σ=10
σ=1
E Electric field
σ Electrical conductivity
n Sample concentration

## Slide 20: FASS in microchannels
Low cond. fluid
High cond. fluid
High cond. fluid
V
E
+
Chien & Burgi, A. Chem 1992
dP/dx
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 21: FASS in microchannels
Low conductivity fluid
Sample ions
Simply calculate mean fluid velocity, and electrophoretic velocity.
Diffusion/dispersion limits the peak enhancement.

## Slide 22: FASS in nanochannels
Same idea, just a smaller channel.
Differences between micro and nano are quite significant.

## Slide 23: Experimental setup
2 Channels: 250 nm x7 microns
1x9 microns

## Slide 24: Raw data 10:1 conductivity ratio

## Slide 25: Micro/nano comparison
10

## Slide 26: Model
Poisson-Nernst-Planck + Navier-Stokes
Use extreme aspect ratio to get simple equations (strip of standard paper 1/8 inch wide, 40 feet long)

## Slide 27: Full formulation 100+ years old
Concentration of positive salt ions,
Concentration of negative salt ions,
Concentration of sample ions,
G
Navier-Stokes for the fluid velocity vector,
Conservation of mass

## Slide 28: Analysis procedure
Make dimensionless, with separate scales for channel height, H, and length, L.
Define
Throw out (carefully) terms with any power of in front of them.
Solve the zeroth order problem.
Go back to equations and throw out terms with or higher.
State the first order problem.
Integrate (or average) across the depth of the channel.

## Slide 29: Zeroth order electrochemical equilibrium
Relative concentration at centerline,
Conc. of positive salt ions = negative
Debye length/channel height. Constant ~ 0.1
Once potential is solved for, concentration of salt ions, conductivity,
and charge density are known.
Integrate w/ B.C.

## Slide 30: Proceeding to next order in
Flow is constant down the channel
Current is constant down the channel.
Conservation of electrical conductivity.
Conservation of sample species.
u is velocity
ρ is charge density
E is electric field
b is mobility (constant)
σ is electrical conductivity
n is concentration of sample
Bar denotes average taken across channel height

## Slide 31: Assume distinct regions yields jump conditions
High cond.
x=0
x=L
L1
L2
High cond.
Region 1
Low cond.
Region 2

## Slide 32: Total pressure & voltage drop
High cond.
L1
L2
High cond.
Region 1
Low cond.
Region 2
Zeroth order velocity field

## Slide 33: Characteristics
1 micron
Enhancement =13
Enhancement =125
Low conductivity
250 nm
Low conductivity
Sample ions
Sample ions
10:1 Conductivity ratio, 1:10mM concentration

## Slide 34: Why is nanoscale different?
High cond.
High cond.
High cond.
High cond.
High cond.
High cond.
Low cond.
Low cond.
Low cond.
X (mm)
y/H
y/H
y/H

## Slide 35: Focusing of sample ions
-
-
Low cond. buffer
High cond. buffer
High cond. buffer
Uσ
Us,low
Us,high
Debye length/Channel Height
Us,high
Uσ
Us,low

## Slide 36: Simple model to experiment
Simple model – 1D, single channel, no PDE, no free parameters
Debye length/Channel Height

## Slide 37: Focusing of conductivity characteristics finite interface
Low conductivity

## Slide 38: Shocks in background concentration
Mani, Zangle, and Santiago. Langmuir, 2009

## Slide 39: Towards quantitative agreement
Add diffusive effects (solve a 1D PDE)
All four channels and sequence of voltages is critical in setting the initial contents of channel, and time dependent electric field in measurement channel.

## Slide 40: Model vs. experiment (16 kV/m)
Model
Exp.
250 nm
1 micron

## Slide 41: Model vs. experiment (32 kV/m)
Model
Exp.
250 nm
1 micron

## Slide 42: Conclusions
Model is very simple, yet predicts all the key trends with no fit parameters.
Future work
  What is the upper limit?
  Can it be useful?
  More detailed model – better quantitative agreement.

## Slide 43: Untested predictions

## Slide 44: Characteristics – 4 channels
1 micron channel
250 nmchannel
Red – location of sample
Blue – location of low conductivity fluid